|  | OK | Add / Adjust | Repair / Replace |  | OK | Add / Adjust | Repair / Replace |
| --- | --- | --- | --- | --- | --- | --- | --- |
| EXTERIOR |  |  |  | SOLUTION TANK |  |  |  |
| Inspect Paint Finish |  |  |  | All Door Latches & Knobs Tight |  |  |  |
| Inspect Doors for Fit, Seal & Adjustment |  |  |  | Clean-Out Doors (no leaks) |  |  |  |
| Hinge Mounts Tight |  |  |  | Solution Delivery Working Properly |  |  |  |
|  |  |  |  | Ball Float Mechanism Functional |  |  |  |
| HOPPER |  |  |  |  |  |  |  |
| Check Caulked Areas of Filter Chamber |  |  |  | UNDER CARRIAGE |  |  |  |
| Filter Shaker Operates Properly |  |  |  | Brooms & Brushes Installed |  |  |  |
| Filter Retainers Tight |  |  |  | Brooms & Scrub Head Raises & Lowers Freely |  |  |  |
| Hopper Hood Sealing Properly |  |  |  | Drain Hose (no leaks) |  |  |  |
| Hopper Flaps Intact & Adjusted to 1/8” from ground |  |  |  | Squeegee Hose Connected |  |  |  |
| Inspect & Test Filters for Leakage |  |  |  |  |  |  |  |
| Safety Arm Fits Properly |  |  |  | OPERATION |  |  |  |
|  |  |  |  | Water Pick-Up |  |  |  |
| ENGINE COMPARTMENT |  |  |  | Squeegee Raises in Reverse |  |  |  |
| Engine Oil Level |  |  |  | Back-Up Alarm Functional (Optional) |  |  |  |
| Air Cleaner Connections Tight |  |  |  | Safety Light Operational (Optional) |  |  |  |
| Engine Belts Tight |  |  |  | Head, Tail & Instrument Lights Function |  |  |  |
| Battery Electrolyte |  |  |  | Noise or Vibration (no abnormal) |  |  |  |
| Battery Cables Tight |  |  |  | Options Function Properly |  |  |  |
| Hydraulic Connections (leaks or seepage) |  |  |  | Main Broom, Side Broom Adjusted Properly |  |  |  |
| Coolant Level |  |  |  | Scrub Brushes Adjusted Correctly |  |  |  |
|  |  |  |  | Sweeping Performance |  |  |  |
| IMPELLER COMPARTMENT |  |  |  | Squeegee flair set correct |  |  |  |
| Hydraulic Fluid Level |  |  |  |  |  |  |  |
| Hydraulic Connections (leaks or seepage) |  |  |  | MISCELLANEOUS |  |  |  |
|  |  |  |  | Unnecessary Tags & Stickers Removed |  |  |  |
| OPERATOR COMPARTMENT |  |  |  | Correct Manual with Unit |  |  |  |
| Parking Brake Adjustment |  |  |  | Warning and Safety Decals in Place |  |  |  |
| Choke Cable Movement (as appropriate) |  |  |  | Solution Tank Drained |  |  |  |
| Horn Operation |  |  |  | Recovery Tank Drained & Flushed |  |  |  |
| Throttle Operation |  |  |  | Hopper Cleaned |  |  |  |
| RTR Lights Adjusted Correctly |  |  |  | Unit Washed & Cleaned |  |  |  |
| All Instruments & Gauges Function Properly |  |  |  | Fuel Level OK |  |  |  |
|  |  |  |  | POWERBOSS COMMITMENT TO EXCELLENCE |
| NOTES & COMMENTS (Include Pictures when possible) |  |  |  |  |
|  |  |  |  | WE HEREBY CERTIFY THAT ALL ITEMS ON THIS FORM HAVE BEEN CHECKED AND |
|  |  |  |  | CORRECTED FOR PROPER OPERATION AS REQUIRED. |
|  |  |  |  | / / |
|  |  |  |  | TECHNICIANS SIGNATURE / DATE SERVICE MANAGERS SIGNATURE / DATE |
|  |  |  |  | SUBMIT THIS FORM TO warranty@powerboss.com |
|  |  |  |  | SERIAL NUMBER | DEALER | MODEL NUMBER |